## Slide 1: Lecture # 5 COMPOUND DC GENERATOR

## Slide 2: COMPOUND DC GENERATOR
32
When the series field is used along with the shunt field, we have a
compound dc generator.
The purpose of the compound generator is to improve the load characteristics of the shunt generator as load increases.
(b) Short Shunt
(a) Long Shunt
Types of compound dc generators

## Slide 3: COMPOUND DC GENERATOR
Two types of compound dc generators:
  Differential compound generator: the series field polarity opposes the shunt field polarity.
  Cumulative compound generator: both the shunt field and series field have the same polarity and the series field aids the shunt field (add flux together).
Differential Compound DC Generator:
  As the current I passes through the series field, the total flux will go down rapidly since the polarities of the series and shunt fields oppose each other. Therefore, Eg will decrease.
  As load increases, the voltage will drop sharply because of the flux decrease.
  It is good for constant-current applications.

## Slide 4: COMPOUND DC GENERATOR
Cumulative Compound DC Generator:
  Both the shunt field and series field have the same polarity and the series
field aids the shunt field (add flux together).
  The flux will not decrease as sharp as it did with differential compound generator.
Types of Cumulative Compound DC Generator:
  Over compounding: the full-load voltage is larger than no-load voltage when the series field is strong.
  Flat compounding: the full-load
voltage is relatively equal to
no-load voltage.
  Under compounding: the full-load voltage is less than the
no-load voltage.

## Slide 5: COMPOUND DC GENERATOR
The load current:
Po = Vt . IL , then
IL = Po/Vt = 5000/125 = 40A
The field current:
If = Vf/Rf = Vt/Rf = 125/125 = 1A
The armature current: [KCL] Ia = IL + If = 41A
Sol.
Example 6:
A long shunt compound generator rated 5-KW, 125-V has an efficiency of 80% when supplying rated load. If Rf = 125  , Ra = 0.2 , and Rs = 0.05 , find at full- load:
+
Vf
_

## Slide 6: COMPOUND DC GENERATOR
Example 6:
A long shunt compound generator rated 5-KW, 125-V has an efficiency of 80% when supplying rated load. If Rf = 125  , Ra = 0.2 , and Rs = 0.05 , find at full- load:
Sol.
The copper loss:
Pcu  Rf I2  R  R  I2
f a s a
Pcu  125x12  (0.2  0.05)x412  545.25 W
The stray power loss:
Po
Pst
Pcu
Pconv
%  Po 100  Pi  Po 100  5000 100  6250 W Pi  80
Pi = Po + Pcu + Pst  Pst = Pi – Po – Pcu Pi
Pst = 6250 – 5000 – 545.25 = 704.75 W

## Slide 7: COMPOUND DC GENERATOR
a) The load current:
Po = Vt . IL , then
IL = Po / Vt = (3103)/200 = 15 A
b) The shunt field current: Solve for Vf : [KVL] Loop 1
– Vf + Rs IL + Vt = 0 , then
Vf = Rs IL + V
t
f
V = (0.2 15) + 200=203 V
If = Vf / Rf = 203/100 = 2.03 A
c) The armature current: [KCL]
Ia = IL + If = 15+2.03=17.03 A
Sol.
+
Vf
Example 7:
A short shunt compound generator rated 3-KW, 200-V has stray losses of 120-W at full load. If Rf = 100  , Ra = 0.9 , and Rs = 0.2 , find at full- load:
Loop 2
Loop 1

## Slide 8: COMPOUND DC GENERATOR
Pcu  Rf I2  R I2  R I2
f a a s L
Pcu  412  261 45  718 W
g) The efficiency:
Pi = Pconv + Pst
Pi = 3718 + 120 = 3838 W
%  Po 100  3000 100  78.2 % Pi 3838
or
Pi Po
Pst Pcu
Pconv
Example 7:
A short shunt compound generator rated 3-KW, 200-V has stray losses of 120-W at full load. If Rf = 100  , Ra = 0.9 , and Rs = 0.2 , find at full- load:
Sol.
39
Eg  Ia Ra  Vf
Eg  17.03 0.9  203  218.33 V
The converted power:
P conv = Eg Ia
=218.3317.03 = 3718W
The total copper loss
Pcu  Pconv  Po
Pcu  3718  3.0 103  718W
d) The generated : [KVL] Loop 2
Eg  Ia Ra  Vf  0 , then

## Slide 9: SOLVED PROBLEMS
a) The armature current:
Ia = IL + If = Vt/IL + Vf/If ; Vf = Vt
= (250/12.5) + (250/250) = 21A
The induced emf: (Loop 1)
Eg = Ra Ia + Vt
Eg = (0.24 21) + 250= 255 V
The flux per pole:
   2 2 255  9.83 mWb
778 8 52.36
  Nsyn 2  500  2  52.36 rad / s 60 60
Sol.
+
Vf
Example 8:
An 8-pole dc shunt generator with 778 wave-connected armature conductors and running at 500rpm supplies a load of 12.5 Ω resistance at terminal voltage of 250 V. The armature resistance is 0.24Ω and the field resistance is 250 Ω. Find a) the armature current, b) the induced emf and c) the flux per pole.
2a Eg
Z P 
Eg 
  
2a Z P 
Loop 1
49

## Slide 10: SOLVED PROBLEMS
turns per coil are 8. Knowing that the armature is simplex wave-wound.
a) Since the induced voltage Eg is more than the terminal voltage Vt ; [Eg > Vt], then the dc machine is working as a generator.
g
E  N P    N  a Eg
a P  
 2  240
 N   400
4 10 103  94.25
a
b) I
Ra
Eg  Vt

 240  200  100 A
0.2
Since there are 8 turns in a coil, it means there are 16 active conductors/coil. Hence, the Number of Coils = 400/8 = 50 coils.
Sol.
c)   Nsyn 2  900  2  94.25 rad / s
60 60
a  2Plex  21  2 pathes
Example 9:
A 4-pole, 900 rpm dc machine has a terminal voltage of 220 V and an induced voltage of 240 V at rated speed. The armature circuit resistance is 0.2 Ω. a) Is the machine operating as a generator or a motor ? b) Compute the armature current and
c) the number of armature coils if the air-gap flux/pole is 10 mWb and the armature

## Slide 11: Extra Problems
A generator turning at 200 rad/s develops 252V. As a result of a short in the field winding, the flux drops by 30%. This causes a drop in voltage. How fast should it turn to restore the voltage to its original value?
A 220 V, 10 kW generator has 255 V measured at its terminal under no-load condition.
What is the percent voltage regulation?
A 1 kW, 120 V generator has a full-load regulation of 18%. What voltage should be measured at its terminals at no-load?
A 5 kW, 230 V generator requires 9 hp when supplying rated load. What is the full load
efficiency?
A shunt generator whose no-load voltage is 480 V is connected to a 440 V bus. If Ra = 0.6 
and Rf = 165 , find the power it will supply to the bus?
A 100 kW, 600 V short shunt compound generator has Rf = 300  , Ra = 0.1 , Rs = 0.05 , and constant stray power losses of 2.4 kW. Find the efficiency at full-load.

## Slide 12: Extra Problems
7) For the generator characteristics shown in the figure below, calculate the percent voltage regulation for each generator at full-load current of 12A.
150
100
50
250
200
400
350
300
0
3
6
9
12
15
Vt [V]
IL [A]
Gen. 1
Gen. 2
Gen. 3
Gen. 4